## Slide 1: EV fast charging & mhd granular forecasts for planning
AEIC-WLRA Conference
September 23, 2025

## Slide 2: 1. Background 2. DSA’s Approach 3. Key Data sources 4. DCFC & L2 charging station propensity development 5. MHDV depot, rest stop propensity development 6. key takeaways
CONTENTS

## Slide 3: More charging stations needed to support growing number of evs
Increasing share of new vehicle sales are battery electric vehicles (BEV)
  More DCFC/L2 charging stations need to be built to support the growing demand
Predicting EV charging and MHDV fleets is important to distribution planning:
  Impacts from charging and fleets are more concentrated than impacts from residential EV charging
  Certain states transitioning to 100% electric school bus fleets (New York)
Predicting where future stations will be built and where fleets will electrify is difficult primarily due to a lack of data on charging ports and small number of electric fleets
Growing share of green vehicles among newer model years
Penetration of electric vehicles among all MHDVs remains low

## Slide 4: Dsa’s approach combines top-down forecasts and bottom-up propensities
Higher propensity scores indicates higher probability of adoption
Top-down forecast developed using historical, territory-wide adoption trends
Can be produced for multiple scenarios (e.g., low adoption, policy scenarios)
Calibrated forecasts can be scaled by 8760 normalized load shapes to estimate the hourly impact
8760 modifier forecast can be added to native load forecast
  Quantifies how peak hours change with modifiers
Propensity Scores
Territory-Wide Forecast
Granular Forecast

## Slide 5: We adjusted our approach for charging and fleet propensities
While top-down bottom-up forecasting is still the core of how we predict impacts from stations and fleets, we take a slightly different approach for developing propensities
  DCFC & L2 stations – use session data somehow to incorporate the fact that not all stations see the same amount of traffic
  MHDV fleets – develop propensities for depots and rest stops separately, reflecting the fact that large trucks often refuel at rest stops during their journey

## Slide 6: Primary data sources
Property data
  Business type (e.g., restaurant, shopping mall, dealership, etc.), lot size, square footage
NYSDOT:
  Annual traffic volume by vehicle class
Commercial Parcel Characteristics
Alternative fuels data center (AFDC):
  Current location of DCFC and L2 charging stations
DMV Registration Data
  Number of registered medium and heavy-duty vehicles, school and transit buses by zip code in territory
Current Charging Station and Fleet Presence

## Slide 7: Other useful data sources
Charging session data:
  Telemetry data from charging stations
  Google Places API can be used to ping availability of chargers at hourly intervals
Survey data from businesses with MHDV fleets:
  Fueling and dwelling times
  Fueling patterns (i.e., depot vs. public)
  % of fleet that will be electrified by 2030, 2035, 2040
  Whether the company has an electrification target
  Likelihood of developing an electrification target before 2030
Utilization – Google Places API
Utilization – DCFC Session Data

## Slide 8: Charging station propensity development

## Slide 9: Predicting both future locations and average demand is key for developing a charging granular forecast
Charging Station Locations
Magnitude of Charging Demand
All chargers tied to a commercial property
Certain commercial locations more likely to have a station built than others
Probit model used to produce probabilities of a commercial property hosting a certain type of station (i.e., DCFC/L2)
Reflects the reality that certain stations may have more charging than others
Linear model used to produce estimates of average hourly demand at each commercial site
Important Features Explored:
(1) Traffic volume
(2) Property characteristics (property type, market value, lot size)
(3) Surrounding business counts (i.e., dealerships, retail, restaurants)

## Slide 10: Both modal property type and counts of various business types within 1 km were important features
Important property types included:
Gas stations
Restaurants
Retail
Parking lots
Theaters
Dealerships
Orange dots represent the commercial properties within 1 km of the green dot

## Slide 11: Properties matched to nearest major intersection to estimate average traffic volume
Properties matched to the intersection within NYSDOT traffic geospatial data
Most properties with the farthest distance to a major intersection are on outskirts of PSEG territory

## Slide 12: Average hourly demand estimated from session data
DCFC
L2
115 – Nassau County
118/117 – Central Long Island
119 – Eastern Long Island

## Slide 13: Different sets of features were important for predicting dcfc vs l2 station presence
DCFC
L2
Variables boxed in red indicate significant features

## Slide 14: Model performance for predicting dcfc and l2 station presence
DCFC
L2
We use the area under the curve (AUC) score to evaluate model performance.
AUC score is the area under the ROC curve. The closer the AUC score is to 1, the better the model.
In our analysis, the DCFC model performed better than the L2 model.
AUC: 0.91
AUC: 0.81

## Slide 15: Propensity Scores for DCFC station locations
Highest propensity locations in Hempstead
A few moderately likely locations for DCFC stations in Levittown, Smithtown, Riverhead
Distribution of propensities extremely skewed
Opacity and bubble size increase with higher propensity scores

## Slide 16: Propensity Scores for l2 station locations
Highest propensity locations in Hempstead
A few moderately likely locations for DCFC stations in Smithtown, Southampton
A lot more locations with low-to-mid propensity scores along highways and in city centers
Opacity and bubble size increase with higher propensity scores

## Slide 17: Predicted dcfc hourly demand for commercial locations
Highest average hourly DCFC demand in Nassau County (115XX zip codes)
A clusters spots medium demand scattered throughout Suffolk County

## Slide 18: Predicted L2 hourly demand for commercial locations
Highest average hourly L2 demand in Suffolk County (117XX,118XX zip codes)
Low average hourly demand in Southampton, Westhampton Beach, Riverhead

## Slide 19: predicted station build and demand are inputs for calibration
Annual consumption estimated from predicted average hourly demand for each location
Highest propensity locations are assumed to be built first
Stations are built until the annual consumption across all stations roll up to the total, system-wide forecast
2025 Cumulative Forecast (DCFC)
Top 14 locations for DCFC stations and the associated total GWh in consumption

## Slide 20: Dcfc station build forecast (base scenario)
2025
2035
Stations with highest consumption predicted to be built in Nassau County predominately
Less utilized stations pop up along major highways

## Slide 21: L2 station build forecast (Base Scenario)
2025
2035
Stations with highest consumption predicted to be built in Nassau County, and the western portion of Suffolk County
Cluster of L2 stations show up in Riverhead, Southampton and Westhampton Beach areas, although these stations are predicted to have much less demand

## Slide 22: Mhdv depots and fleets propensity development

## Slide 23: Separate approaches taken for developing depot and rest stop propensity scores
Share of MHDVs registered by zip code
Commercial parcel lot size
  Lot sizes used to split up MHDV registrations within one zip code to multiple commercial parcels – larger parcels assigned more MHDVs
Likelihood of fleet electrification from survey
  % of fleet that will be electrified by 2035
  Likelihood of company developing electrification target before 2030
  Likelihood is at the industry level (i.e., construction, municipal, manufacturing)
Depots
Propensity scoring based on single-unit and combination unit traffic flow at nearest intersection to existing rest stops
Rest stops
Single-unit
Combination-unit

## Slide 24: Incorporating survey results led to decrease in allocation for municipal/governmental industries
Propensity Based Only Current Fleet Locations
Adjusted Using Survey Results
Government/municipal fleet propensities decrease as a result

## Slide 25: MHDV depot propensities scores

## Slide 26: Rest stop propensity scores
Propensities allocated among 14 existing rest stops in Long Island territory
Allocation performed according to amount of CU/SU truck traffic at the nearest intersection of rest stop
Many rest stop locations along Long Island Expressway
Rest stop with highest traffic located on Sunrise Highway

## Slide 27: Key takeaways

## Slide 28: Key takeaways
Building use (e.g., gas station, restaurant, retail) and traffic volume data are important characteristics for predicting station presence
Charging session data is still lacking. It is difficult to parse out the relationship between commercial parcel characteristics (i.e., traffic flow, property type) and utilization with so few data points
Need to adjust approach based on what is available and leverage public data
  For Central Hudson, not much session data available – pivoted to pinging Google Places API for determining hourly utilization
  For PSEG-LI, we were able to leverage survey data to adjust propensities to reflect the reality that not all MHDV fleets will electrify

## Slide 29: Questions?
Candace Yee
Consultant
Demand Side Analytics
cyee@demandsideanalytics.com
310.486.6576